## Slide 1
PIMPRI CHINCHWAD COLLEGE OF ENGINEERING
Department of Computer Science and Engineering (AI & ML) · Academic Year 2026–27
PROJECT SYNOPSIS · REVIEW I
Smart Classroom Infrastructure Monitoring
and Maintenance System
Using Computer Vision and IoT
Presented by
Raghvendra Kotgire — 124B2C006
Anuj Chandak — 124B2C008
Prasanna Pawar — 124B2C011
Project Guide
Dr. P. R. Sonawane
Notes: Good morning. We are presenting SIMMS — a smart classroom infrastructure monitoring and maintenance system that carries a fault from automatic detection all the way to supervisor-verified closure.

## Slide 2
01 PROBLEM
Motivation and Problem Statement
1
SIMMS | Project Synopsis — Review I
An engineering institution runs dozens of classrooms whose lights, fans, boards and furniture are inspected manually and irregularly.
1
Inspection is intermittent
No one watches every room, so a fault persists for days.
2
Reporting is informal
Verbal or register entries — no record of when, to whom, or whether fixed.
3
No accountability trail
Resolution is never recorded, so recurring faults stay invisible.
PROBLEM STATEMENT
To monitor classroom occupancy, board condition and the status of lights and fans using computer vision and IoT sensing; to verify each detected abnormality against multiple sources and raise a maintenance ticket only on a confirmed fault; and to classify, prioritise, assign and track that ticket until supervisor-verified closure.
The gap is not detection capability — it is the absence of a closed loop from observation to verified repair.
Observe › Confirm › Classify › Ticket › Assign › Notify › Repair › Verify › Close
Notes: Sensor-only systems show readings nobody must act on; vision-only systems detect objects but connect them to no one. The project builds the loop across the bottom of this slide.

## Slide 3
02 LITERATURE
Literature Survey and Research Gap
2
SIMMS | Project Synopsis — Review I
# | Study | Method | Limitation
1 | Muzayanah et al. (2024) | OpenCV face detection, fixed absence timer | No sensor corroboration
2 | Kinjarapu et al. (2026) | PIR, face, voice, device signals on Pi | Presence only; no workflow
3 | Niveditha et al. (2023) | PIR, LDR, temperature drive relays | Fixed thresholds; no vision
4 | Monti et al. (2022) | Transfer-learned CNN counting on Pi | Counts only; no condition
5 | Wang; Chen et al. (2023) | CA-YOLOv7 / YOLOv8 behaviour recognition | Analytics of people, not rooms
6 | Zhai et al. (2015) | Occupancy-driven HVAC and lighting | Cannot verify equipment works
7 | Kumar et al. (2026) | PIR, ultrasonic, camera with confirmation | Safety alert, no lifecycle
Enabling references [8]–[14] — edge computing (Shi), YOLOv7 (Wang), CNN defect detection (Cha), ML predictive maintenance (Carvalho), MQTT protocol comparison (Naik), occupancy sensing (Candanedo; Chen).
Research gap
1
Modalities are not fused
Sensor data sits alongside vision output rather than entering one rule.
2
Detection is not connected to resolution
Detection ends at an accuracy figure; maintenance systems begin at manual entry.
3
False-alarm behaviour is not reported
Papers report mAP on curated sets, not spurious alerts during unattended operation.
This project addresses all three: it fuses both signals in every rule, spans detection to verified closure, and reports operational false-alarm rate as a primary result.
Notes: Fourteen papers are reviewed in the synopsis. The seven on the left are the closest classroom and building systems; each stops at detection, control or presence. The third gap is the unusual one — we treat false alarms as a headline result.

## Slide 4
03 OBJECTIVES
Aim, Objectives and Scope
3
SIMMS | Project Synopsis — Review I
AIM
To detect classroom infrastructure and electrical faults using edge-based computer vision and IoT sensing, and to manage each confirmed fault through a digital workflow to supervisor-verified closure.
Core objectives — committed deliverables
Periodically capture and analyse classroom condition on an edge computing device
Determine seat-level occupancy using person detection over calibrated seat regions
Monitor light and fan status and electrical parameters using IoT sensors
Confirm, de-duplicate and debounce detections before raising a ticket
Automatically classify, prioritise and assign maintenance tickets
EXTENDED — AFTER CORE IS STABLE
Fan rotation verification · furniture anomaly and damage detection · recurring-fault analytics · automated reports · multi-classroom demonstration
NON-GOALS
No facial recognition or identification · no continuous recording or cloud upload of frames · no attendance system · no switching of live classroom loads
Notes: Eleven committed objectives and six extended ones. The non-goals are stated deliberately so that scope stays fixed and the privacy position is unambiguous.

## Slide 5
04 PROPOSED SYSTEM
System Architecture
4
SIMMS | Project Synopsis — Review I
CLASSROOM (EDGE)
Camera + Raspberry Pi 4
1 frame / 30–60 s · person detection,
seat-ROI occupancy, board ink ratio,
blurred evidence capture
ESP32 sensor node
sample / 5 s · PZEM-004T, CT clamp,
DHT11, LDR — V, I, P, PF, energy
JSON observations only — no raw video leaves the room
MQTT
SERVER
Backend — FastAPI
Ingest and persist observations
Confirmation · debounce · de-duplication
Rule engine and classification
Ticket lifecycle and assignment
Health score · REST API
Web Push and Telegram
STORE AND CLIENT
PostgreSQL 16
State and full event history
React PWA
Supervisor · staff · admin
calibration screens
Periodic inspection, not real-time video — one frame every 30–60 s keeps the Raspberry Pi under 7 % duty cycle, removes the need for a GPU, and makes the privacy position defensible.
Notes: The key architectural decision is on the bottom bar: classroom infrastructure changes over minutes, not milliseconds, so we sample rather than stream.

## Slide 6
05 PROPOSED SYSTEM
Detection Modules
5
SIMMS | Project Synopsis — Review I
Occupancy
Pretrained YOLO, person class only, tested against calibrated seat ROIs.
Seat geometry comes from calibration — no seat detector to train.
Board condition
Perspective warp, adaptive threshold, morphological opening, ink-pixel ratio.
A measurement, not a perception problem — explainable and tunable on site.
Electrical status
PZEM-004T on the demo panel plus a CT clamp on the fan branch.
Current bands are learned at commissioning, not hard-coded.
Energy wastage
Occupancy = 0 for ≥ 10 min AND measured load above threshold.
Requires both modalities — neither alone separates waste from use.
Contextual coupling — the operative idea
A board covered in writing during an active lecture is normal and raises nothing. The same board with the room confirmed vacant for ten minutes becomes a cleaning task. Occupancy contextualises board state; occupancy contextualises electrical load.
Notes: This slide answers the obvious question — why use both a camera and sensors? Because no rule here thresholds a single signal.

## Slide 7
06 PROPOSED SYSTEM
Confirmation, De-duplication and Ticket Lifecycle
6
SIMMS | Project Synopsis — Review I
A raw detection is not an event, and an event is not a ticket. Three mechanisms in sequence — the project's principal reliability contribution.
a
Temporal confirmation
A sliding window per (classroom, detector, target). Thresholds are asymmetric — slower to raise a fault than to clear one.
b
De-duplication by signature
Confirmed faults reduce to (classroom, issue type, target, calibration version). A repeat increments a counter, not a second ticket.
c
Cooldown and auto-resolution
A closed signature is suppressed for 30 minutes. A fault clearing before anyone acts closes as AUTO_RESOLVED.
Window 5 obs.
Raise 4 of 5
Clear 3 of 5
Confidence ≥ 0.55
Cooldown 30 min
Sample 60 s / 5 s
Ticket lifecycle
NEW
ASSIGNED
IN_PROGRESS
RESOLVED
VERIFIED
CLOSED
REOPENED — supervisor rejects the repair · AUTO_RESOLVED — fault clears before anyone acts
Staff cannot close their own tickets — RESOLVED → VERIFIED requires supervisor action, which is what makes the record an accountability trail.
Routing — Electrical → Electrical Maintenance (2 h / 8 h) · Cleaning → Housekeeping (24 h) · Furniture → Furniture Maintenance (8 h) · Energy → Electrical Supervisor (8 h)
Notes: If the examiners ask one technical question, expect it here. Four of five observations must agree to raise a fault but only three of five to clear it — the asymmetry biases the system against false tickets. De-duplication prevents forty tickets for one broken fan in a day.

## Slide 8
07 OUTCOMES
Expected Outcomes and Performance Targets
7
SIMMS | Project Synopsis — Review I
≤ 1
false ticket per
classroom per day
≥ 92 %
seat-level occupancy
accuracy
≤ 6 min
from fault onset
to ticket
≤ 3 s
edge inference
per cycle
Parameter | Target | Measurement method
Occupancy count error | MAE ≤ 2 seats | Against manual count, 100+ frames
Seat-level occupancy accuracy | ≥ 92 % | Per-ROI ground truth, held-out set
Board state agreement | ≥ 85 % | Versus two independent annotators
Light ON/OFF detection | ≥ 98 % | Controlled switching trials
False ticket rate | ≤ 1 per room per day | 7-day continuous unattended run
Missed fault rate | ≤ 5 % | Injected fault trials
Ticket-to-notification latency | ≤ 10 s | Server log versus device receipt
DELIVERABLES
Single-classroom prototype
Automatic classified and routed tickets
Installable PWA with push notifications
Measured accuracy and false-alarm rate
Complete digital audit trail
These are design targets to be validated experimentally, not claimed results. Where a target is missed, the measured value will be reported with an analysis of the cause.
Prototype cost approximately Rs. 5,460 · hosting cost nil — the full stack runs on one machine on the college LAN.
Notes: Frames per second is deliberately excluded as a metric — the system samples once every 30 to 60 seconds by design, so a high frame rate would mean nothing. The false-ticket rate is measured over a seven-day unattended run, not during a demonstration.

## Slide 9
CONCLUSION
Two contributions
1
Every decision rule fuses a vision signal with a sensor signal
Occupancy contextualises board state; occupancy contextualises electrical load. The system separates legitimate use from genuine fault in a way neither modality achieves alone.
2
The system is engineered and evaluated to be trusted
Explicit confirmation, de-duplication and cooldown logic — and a reported measure of how rarely it raises problems that do not exist, alongside how well it detects the ones that do.
Its contribution is not object detection in a classroom, which is well established — it is the closed loop, and the evidence that the loop can be trusted.
Thank you
Questions and suggestions welcome
8
Notes: To close: the novelty is not that we detect people in a classroom. It is that a fault travels automatically from detection to verified closure, and that we measure how often it does so wrongly. Thank you — we are happy to take questions.